## Slide 1
Soil and Materials Engineers, Inc.
consultants in the geosciences, materials and the environment
James Harless, PhD, CHMM
Vice President / Principal
Ohio
Michigan
Indiana
www.sme-usa.com
CASE STUDY
Living the Value Proposition

## Slide 3: OVERVIEW
Project Overview
Environmental Services
Geotechnical Services
CoMET Services
Sustainability
Value Added Summary

## Slide 4: PROJECT OVERVIEW

## Slide 5: DEVELOPMENT
Wind tower manufacturing
48-acre site
100,000 sq. ft. factory + 10,000 sq. ft. offices
Heavy products - high floor, pavement and ground loads
Requires road, rail and water transportation facilities
$19,000,000 startup

## Slide 6: ADDING VALUE
FINANCE
SUSTAINABILITY
ENVIRO
GEOTECH
CoMET

## Slide 7: ADDING VALUE
NOT
COMMODITY SERVICES
CONSULTING SERVICES

## Slide 8: ADDING VALUE
Big picture vision
Creative solutions
Integrated higher level services at lower overall costs
Incorporating sustainability
Finding the money

## Slide 9: SITE CONDITIONS
Industrial waste landfill (1950s – 1975)
  Foundry sand
  Coal tar
  Colorful chemical wastes
Groundwater/leachate contamination
“Soil” contamination
  Human contact
  Vapor intrusion

## Slide 10: CHALLENGES
Geotechnical
  Unconsolidated fill
  Can’t penetrate underlying clay
  High foundation and pavement loads
Environmental
  Human exposure mitigation (entire site)
  Vapor intrusion mitigation (entire building)
Minimizing and financing the extra costs

## Slide 11: GEOTECHNICAL SERVICES

## Slide 12: GEOTECHNICAL SERVICES
Assessment
Building support design
Pavement and external loads design

## Slide 13: FOUNDATION STRATEGY
Driven conventional piles
Soil stabilization
  Controlled Modulus Columns (CMC)
  Rammed Aggregate Piers

## Slide 14: CMC INSTALLATION
Share of the load between column and soil
100% of the load in the piles.
No load in the soil
Load Transfer Area

## Slide 15: PAVEMENT AND LAYDOWN AREAS

## Slide 16: GEOTECHNICAL SERVICES
All geotechnical services were classified as brownfield redevelopment response actions to make them eligible for brownfield financing

## Slide 17: ENVIRONMENTAL SERVICES

## Slide 18: ENVIRONMENTAL SERVICES
Due diligence and human exposure assessments
Safe use designs
  Contact exposure barrier
  Vapor intrusion barrier
  Storm water pond liners
Waste relocation compliance
Brownfield redevelopment financing

## Slide 19: BROWNFIELD COSTS
ENVIRONMENTAL
Assessment and due diligence………………….. $70,000
Site preparation and excess fill management.. $225,000
Contact exposure barrier……………………… $2,600,000
Vapor intrusion barrier…………………………… $625,000
Storm water detention pond liners…………….. $170,000
Environmental management and monitoring... $160,000
SBA 504 loan environmental documentation…. $10,000

## Slide 20: BROWNFIELD COSTS
NON-ENVIRONMENTAL
Geotechnical engineering………………………… $55,000
Soil stabilization………………………………… $1,200,000
INFRASTRUCTURE
Water main loop…………………………………… $350,000
Railroad spur………………………………………. $525,000
Railroad trunk improvements………………… $1,000,000
Dock infrastructure improvements………….. $1,500,000

## Slide 21: BROWNFIELD FINANCING
Environmental…………... $5,200,000 (including non-environmental)
State assessment grant………... $70,000
State brownfield grant……… $1,000,000
State brownfield loan……….. $1,000,000
EPA RLF Grant loan (DCC)…$2,000,000
State/local brownfield TIF….. $4,130,000

## Slide 22: BROWNFIELD FINANCING
Infrastructure…………….$3,375,000
State DOT grant………………... $800,000
State/local brownfield TIF……. $900,000
Other infrastructure grants… $1,000,000
Unfunded ……………………….. $675,000

## Slide 23: OTHER ENVIRO SERVICES
Project services coordination
Brownfield financing management and documentation
External financing support (e.g. SBA)
Project visibility

## Slide 24: CoMET SERVICES
CMC installation
Exposure barrier installation
Foundations
Storm water pond liners
Vapor intrusion mitigation system
Foundations
Tried to save money – no CoMET
Couldn’t pass city inspection
SME used pulsed radar and ultrasonic testing to retroactively verify foundation construction and placements over CMCs and construction of load transfer area

## Slide 25: CoMET SERVICES
All CoMET services, except for foundations, were classified as part of brownfield redevelopment response actions to make them eligible for brownfield financing
Cross-trained staff monitored multiple operations simultaneously to save money

## Slide 26: SUSTAINABILITY
Wind power for the plant
Excess fill retained on site
Soil stabilization with no spoils
Minimal commuting
Minimal on-site engine idling
Use of biodiesel

## Slide 27: VALUE ADDED
FINANCE
SUSTAINABILITY
ENVIRO
GEOTECH
CoMET
Complex due diligence and regulatory compliance
Experience with large, complex brownfield redevelopments
Practical exposure mitigation expertise
Creative solutions for complex site
Close coordination with environmental and brownfield issues
HAZWOPER trained staff
Cross-trained staff also performed environmental monitoring
Internally coordinated services
Team communication – identified and solved problems quickly
Minimal excess fill from construction activities
No off-site disposal
Identified green operational practices
Acquired and managed >$6,000,000 brownfield financing
Supported acquisition of $5,000,000 project financing
Brownfield financing for site development activities
Combined environmental-CoMET monitoring services
Creative, cost-effective solutions to multiple problems

## Slide 28: VENTOWER

## Slide 29
Soil and Materials Engineers, Inc.
consultants in the geosciences, materials and the environment
James Harless, PhD, CHMM
Vice President / Principal
Ohio
Michigan
Indiana
www.sme-usa.com
CASE STUDY
Living the Value Proposition