## Slide 1: VALUE ADDED: FIRST and LAST
A CASE HISTORY FOR GEOTECHNICAL ENGINEERING ADDING VALUE TO A BUILDING PROJECT
Michael T. Lustig, P.E.
Geotechnical Services, Inc.

## Slide 2: Adding Value to Building X
Project Description / History
The Role of Geotechnical Engineering
Summary of Value Added to this Project

## Slide 3: Building X Description & History
Single Story, Slab-On-Grade, Precast Concrete Wall Panels
36,000 square feet, structure completed in 2007
No geotechnical investigation performed before construction
All foundations supported on 2 - 3 feet of granular structural backfill

## Slide 4: Building X Description & History
Two years after completion, building floors settle 3” to 4”
Building structure shows little evidence of distress
Forensic investigations reveal layer of man-made fill and organic materials to 15 feet below floor

## Slide 6: The Proposed Solution
Remedial solution was to install over 300 micropiles extended to underlying bearing stratum
Remove part of existing floors and support on micropiles
Leave part of existing floors on micropiles and apply topping

## Slide 7: Geotechnical Engineering Solution
Contractor won project based on conventional micropile design
Client retained GSI to provide design and testing to meet specifications for two conditions, floors and columns
GSI approached design using a grouted pin pile and a helical pile

## Slide 8: Micropile Design

## Slide 10: Helical Pile Design

## Slide 12: Geotechnical Engineering Solution
Client and GSI conducted full scale load tests of each pile type at two locations within the building
Sound geotechnical engineering combined with load test analysis assured safe and economical designs

## Slide 14: An Ounce of Prevention is Worth...
Estimated initial building cost: $5 million
Estimated micropile installation cost: $1 million
Estimated floor replacement/topping cost: $250,000
Estimated administrative costs: $200,000
All remedial work performed nights and weekends - spanned 6 months

## Slide 15: The Value of Geotechnical Engineering to Building X
Lack of initial geotechnical investigation added risk and cost to building
Use of helical micropiles allowed client to beat schedule in some areas – CM and Client appreciated
Full scale load tests assured safe design –SE was satisfied

## Slide 16: The Value of Geotechnical Engineering to Building X
Load tests provided basis for quality control during remediation – helped Testing Agency meet goals
Good geotechnical engineering provided economical micropile designs - helped Client make his bid